## Slide 1
Probabilistic Robot Localization
Kalman Filter · Extended Kalman Filter · Particle Filter
TurtleBot3 Waffle — ROS 2 Jazzy — Gazebo
SPECIAL TASK 2510331009
·
Particle Degeneration Analysis
Rainhard Wipp
M.Sc. Robotics Engineering
FH Technikum Wien
Probabilistic Robotics (PRO)

## Slide 2
AGENDA
01
System & Filter Overview
02
Experimental Setup & Landmark Correction
03
Q / R Sensitivity Study
04
Special Task 2510331009 — Particle Degeneration
05
Discussion, Status & Takeaways

## Slide 3
Problem Statement
Mobile robots must estimate their pose under uncertain motion and noisy sensing
Three classical probabilistic state estimators: KF, EKF, Particle Filter — all implemented on one platform with identical inputs
Special Task 2510331009: disable PF resampling and analyze particle degeneration
Platform
TurtleBot3 Waffle
Framework
ROS 2 Jazzy · Nav2 · Gazebo
Language
C++ (rclcpp, Eigen3) + Python 3
State vector
μ = [x, y, θ]ᵀ (odom frame)
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 4
System Architecture — ROS 2 Nodes
Single ros2 launch starts the full pipeline: Gazebo + Nav2 (0 s) → Filters + RViz + Logger (5 s) → AutoNav (10 s)
Node
Executable
Subscribes
Publishes
Kalman Filter
kf_node
/cmd_vel, /odom, /scan
/pose_kf
Extended KF
ekf_node
/cmd_vel, /odom, /scan
/pose_ekf
Particle Filter
pf_node
/cmd_vel, /odom, /scan
/pose_pf, /pf_particles, /n_eff
Data Logger
data_logger
/odom, /pose_kf, /pose_ekf, /pose_pf, /n_eff
CSV file
AutoNav
auto_nav
—
/initialpose, Nav2 goals
State vector (all filters): μ = [x, y, θ]ᵀ — reference frame: odom
Launch args: pf:=true resampling:=false sigma_process:=.. sigma_meas:=..
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 5
Filters at a Glance
Kalman Filter
Extended KF
Particle Filter
Belief
Gaussian (μ, Σ)
Gaussian (μ, Σ)
N = 500 weighted particles
Prediction
Linearized B matrix cos/sin of θ — accepted approx.
Exact nonlinear g(u, μ) + Jacobian G — no linearization error
Sample x_t^m ~ p(x_t | u_t, x_{t-1}^m) Gaussian noise on v, ω
Correction
C = I₃ vs /odom + linearized landmark Jacobian
H = I₃ vs /odom + landmark Jacobian Hⱼ
Importance weights w p(z | x^m); odom + landmark
Reference
Thrun Table 3.1
Thrun Table 3.3 / 7.2
Thrun Table 4.3 / 4.4
All three filters share the same landmark-based correction → differences come purely from prediction & belief representation
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 6
Shared Landmark-Based Correction
One shared landmark map (landmark_map.hpp) for all three filters — identical correction input, fair comparison
Range-only measurement model — expected bearing from pose estimate indexes into /scan for measured range
Gating: |r_meas − r_exp| ≤ 0.30 m accepted as valid; σ_r = 0.12 m
Two-stage correction: (1) full-state update vs /odom, then (2) sequential 1D range update per visible landmark
Measurement model
h(μ, mⱼ) = ‖mⱼ − [x, y]‖
Gate & noise
LM_GATE_M = 0.30 m LM_SIGMA_R = 0.12 m
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 7
Experimental Setup
Spawn pose: (−1.96, −0.5, 0°) in map frame = odom origin
AutoNav drives a fixed 8-waypoint loop across 4 unique positions — ~3.6 m diameter
Ground truth proxy: /odom (Gazebo) — same caveat applies equally to all filters
Identical route, timing, and sensor stream fed to KF, EKF, and PF on every run
WAYPOINTS
WP1/6 N ( 0.0, 1.8)
WP2/5/8 W (−1.8, 0.0)
WP3/7 S ( 0.0, −1.8)
WP4 E ( 1.8, 0.0)
DEFAULT PARAMETERS
σ_process
0.01
σ_meas
0.10
num_particles
500
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 8
RViz2 Visualization
Particle cloud — PF belief distribution
Laser scan returns
Landmark markers (yellow spheres)
Pose estimate arrow + costmap boundary
Captured during exploratory run — included to satisfy the RViz2 visualization requirement
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 9
Baseline Filter Comparison (Resampling ON)
RMSE vs /odom
KF = 0.047 m
EKF = 0.047 m
PF = 0.047 m
All three trajectories closely overlap with /odom ground truth across the full 8-waypoint loop
PF covariance trace visibly lower — particle-based estimate tends to underestimate once particles cluster
N_eff/N ≈ 1.0 throughout — healthy particle diversity maintained
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 10
Q / R Sensitivity Study
Vary process noise (Q, model confidence) and measurement noise (R, sensor trust) independently
5 runs total: Baseline + low/high σ_process + low/high σ_meas — same route and landmark map throughout
Run
σ_process
σ_meas
Baseline
0.01
0.10
Low proc. noise
0.001
0.10
High proc. noise
0.10
0.10
Low meas. noise
0.01
0.01
High meas. noise
0.01
0.50
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 11
Q / R Results — Trajectories · RMSE · Covariance
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 12
Q / R Sensitivity — Summary
Run
σ_proc
σ_meas
KF
EKF
PF
Baseline
0.01
0.10
0.047
0.047
0.047
Low σ_process
0.001
0.10
0.039
0.037
0.036
High σ_process
0.10
0.10
0.045
0.045
0.041
Low σ_meas
0.01
0.01
0.006
0.006
0.046
High σ_meas
0.01
0.50
0.073
0.069
0.028
σ_meas=0.01: KF/EKF RMSE collapses to 0.006 m — circularity artifact (filter trusts /odom almost unconditionally)
σ_meas=0.5: KF/EKF rise to ~0.07 m; PF stays at 0.028 m — non-parametric PF is more robust to high measurement uncertainty
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 13
SPECIAL TASK 2510331009
Disabling PF Resampling & Analyzing Particle Degeneration
What happens to particle diversity and filter robustness when low-weight particles are never replaced?

## Slide 14
Special Task: Definition
Task 2510331009: "Run the PF with reduced or no resampling" — implemented as a full on/off toggle via ROS 2 parameter ( resampling:=false)
Resampling is the textbook mechanism that prevents the degeneracy problem in Sequential Importance Sampling (SIR) filters
Without it, all probability mass is expected to concentrate on a single particle — weight collapse
Research question
"What happens to particle diversity and filter robustness when low-weight particles are never replaced?"
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 15
Systematic Resampling (Thrun Table 4.4)
1
Build the cumulative weight sum over all N particles
2
Draw a single random offset r ~ U[0, 1/N)
3
For i = 0..N−1: pick the particle at cumulative position r + i/N
Result: high-weight particles duplicated; low-weight dropped; all weights reset to 1/N — O(N), low-variance
Triggered every correction step when resampling = true
# Thrun (2006) Table 4.4
c[1] = w[1]
for i = 2..N:
c[i] = c[i-1] + w[i]
r ~ U[0, 1/N)
for i = 1..N:
u = r + (i-1)/N
pick j: c[j] ≥ u
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 16
Particle Degeneration & N_eff
Without resampling, particle weights are only multiplied — never reset → diverge monotonically over time
Particles with even slightly lower likelihood are exponentially suppressed and never replaced
N_eff computed before the resampling decision → reflects true particle health regardless of whether resampling runs
N_eff = 1 / Σ wᵢ²
∈ [1, N]
N_eff → N
Uniform weights (ideal)
N_eff → 1
Single particle dominates (full degeneration)
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 17
Special Task — Experiment Design
Two full runs on the identical 8-waypoint route: Resampling ON (baseline) vs. OFF (Special Task)
Identical Q/R defaults, landmark map, and N = 500 particles for both runs
/n_eff and /pose_pf logged throughout by data_logger — timestamped CSV per run
Compared via plot_n_eff.py : N_eff/N over time + cumulative RMSE, both runs overlaid on the same axes
Resampling ON (baseline)
./run_experiments.sh --with-resampling
Resampling OFF (Special Task)
./run_experiments.sh --without-resampling
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 18
Results — N_eff Collapse
Resampling ON
N_eff/N ≈ 1.0 throughout the entire ~110 s run, with brief dips at landmark corrections
Resampling OFF
N_eff/N collapses from ≈ 1.0 to ≈ 0.0 within ~20 seconds — numerical zero for the rest of the run
Matches the theoretical prediction: without resampling, degeneration is fast and irreversible
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 19
Results — RMSE & Key Insight
Resampling ON
0.049 m
cumulative RMSE
Resampling OFF
0.076 m
cumulative RMSE (+55%)
The single surviving particle keeps integrating odometry — RMSE alone still looks "reasonable" after full degeneration
The filter has lost its uncertainty representation — cannot express ambiguity or recover from drift
KEY INSIGHT
RMSE is an insufficient diagnostic on its own.
N_eff is required to detect degeneration — a collapsed PF still reports a confident-looking pose and covariance.
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 20
Discussion & Interpretation
Resampling trades short-term particle diversity for long-term robustness — classic bias/variance tradeoff in SIR filters
Without resampling, the PF degrades into a de-facto single-hypothesis filter , losing multi-modality and recovery from ambiguous data association
Practical risk: a degenerated filter still reports a confident-looking pose and covariance — failure goes undetected without explicitly monitoring N_eff
Connects to Thrun (2006), Ch. 4.3: the degeneracy problem is the textbook motivation for resampling in SIR filters
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 21
Limitations
Single run per condition — exact degeneration timing depends on the specific random noise realization
Binary on/off only — no intermediate strategy tested (e.g. threshold-based resampling at N_eff/N < 0.5)
Ground truth is /odom — the same circularity caveat applies as in the Q/R study
Short route (~110 s) — degeneration effects over much longer missions remain untested
Possible extension: threshold-based resampling (resample only when N_eff/N < 0.5) to study an intermediate strategy
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 22
Implementation & Experiment Status
KF
EKF
PF
Prediction step
✓
✓
✓
Correction (odom)
✓
✓
✓
Correction (landmarks)
✓
✓
✓
Full 3×3 covariance
✓
✓
✓
RViz visualization
✓
✓
✓
Timestamp check (stale odom)
✓
✓
—
Tunable Q/R
✓
✓
✓
EXPERIMENTS COMPLETED
✓
Ground truth RMSE vs /odom
✓
Covariance trace visualization
✓
Landmark detection (shared map)
✓
Special Task: N_eff with vs. without resampling
✓
σ_process variation (4 runs)
✓
σ_meas variation (4 runs)
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 23
KEY TAKEAWAYS
KF, EKF, and PF perform near-identically under benign noise on this shared, landmark-augmented setup — differences emerge mainly under high measurement uncertainty, where PF is most robust
Resampling prevents particle degeneration — disabling it causes near-total weight collapse (N_eff/N: 1.0 → ~0.0) within ~20 seconds
RMSE alone does not reveal degeneration — the surviving particle can still track odometry well short-term; N_eff is an essential complementary diagnostic

## Slide 24
References
Thrun, S., Burgard, W., Fox, D. (2006). Probabilistic Robotics. MIT Press.
Table 3.1 — Kalman Filter
Table 3.3 / 7.2 — EKF / EKF Localization
Table 4.3 — Particle Filter (MCL)
Table 4.4 — Systematic Resampling
Nav2 Documentation
docs.nav2.org
ROS 2 Jazzy Documentation
docs.ros.org/en/jazzy
Source code
github.com/Raini20/PROLB_R
PROLB_R — Special Task 2510331009
Rainhard Wipp · FH Technikum Wien

## Slide 25
Thank You
Questions?
Rainhard Wipp · M.Sc. Robotics Engineering · FH Technikum Wien
github.com/Raini20/PROLB_R